## Slide 1: Embedded Systems: Problem solving

## Slide 2: Problem solving flowchart one component
start
does “Hello World!” work?
back to ”Hello World!” example on standard image
end
is the relevant code being executed?
check:
interrupt settings
blocking code
hardware setup
check:
registers settings
reduce to simplest POC possible
hardware setup
yes
no / don’t know
yes
no
Note:
With multiple problems it might be needed to run through the flowchart multiple times
Discussion:
How can an incorrect hardware setup result in code not being executed?
Notes: Notes
The flowchart is not exhaustive, but can serve well in many cases.
If the hardware setup is incorrect, it might result in code not being executed like code in an interrupt handler.
For finding the cause of a problem one can use a fishbone diagram, see https://whatis.techtarget.com/definition/fishbone-diagram. This is a brainstorm like technique used for complex problems. It might be more suited for in the industry project.

## Slide 3: Problem solving flowchart multiple components
start
do components work in isolation?
go to debugging one component flowchart
end
is the relevant code being executed?
check:
thread and interrupt priority
blocking code
hardware changes
check:
input data for relevant component
global resources
memory usage
hardware changes
yes
no / don’t know
yes
no
Note:
With multiple problems it might be needed to run through the flowchart multiple times
When the hardware changes, first test again using single components!
Notes: Notes
The flowchart is not exhaustive, but can serve well in many cases.
If the hardware setup is incorrect, it might result in code not being executed like code in an interrupt handler.
For finding the cause of a problem one can use a fishbone diagram, see https://whatis.techtarget.com/definition/fishbone-diagram. This is a brainstorm like technique used for complex problems. It might be more suited for in the industry project.

## Slide 4: How do I... Check for code execution?
Use debugger / set breakpoint
Use HAL_UART_Transmit()
Notes:
See https://sourceware.org/gdb/current/onlinedocs/gdb/
When debugging disable compiler optimization.
HAL_UART_Transmit is a blocking function
See Speaker Notes for details
Notes: Notes
For use of GDB, see https://sourceware.org/gdb/current/onlinedocs/gdb/.
When debugging it might be needed to disable compiler optimization. This can be done by changing the line ‘OPT = -Og’ into ‘OPT = -O0’ in the Makefile.
There is also HAL_UART_Transmit_IT() which is interrupt based. See https://stm32.programmingpedia.net/en/tutorial/9707/uart-universal-asynchronous-receiver-transmitter-serial-communication.

## Slide 5: How do I... Check for interrupt code execution?
Use debugger / set breakpoint
Use HAL_UART_Transmit()
Use on-board LED (like RX and TX LED on an Arduino board)
Do not forget to reset the interrupt flag!
Notes:
HAL_UART_Transmit will have a big impact on timing!
See Speaker Notes for details.
Notes: Notes
For debugging purposes it is possible to use HAL_UART_Transmit() in an interrupt handler. Because HAL_UART_Transmit() is a blocking function, it will have a big impact on timing, especially at low baud rates! Do not forget to remove it when debugging is done.
Sometimes it can be convenient to use the on-board LED to check if the interrupt handler is being executed. One example might to toggle the LED when a timer interrupt occurs. This way it is immediately visible when there is something wrong with the timer. Toggling a LED does not have a great impact on execution timing and can be possibly left in even in production code so one can always see if the system runs. A similar example is the RX and TX LED on an Arduino board.
If the interrupt flag is not reset within the interrupt handler the interrupt handler will be called again and again, preventing the main program to run!

## Slide 6: How do I... Check global resources?
Check if register settings do not have side effects
Use debugger to set memory watch
Notes:
See Speaker Notes for details.
Discussion:
What kind of side effects can occur when setting bits in a register?
How can global resources be a problem?
How can a memory watch be used here?
Notes: Notes
Global resources can be a problem when they are used by multiple components. One example is that for the NUCLEO-F303RE board external interrupt 5 .. 9 share the same interrupt handler.
When setting bits in a register make sure other bits are left untouched, otherwise side effects might occur!
Setting a memory watch can be very useful when a global resource like a timer control register seems to be overwritten. This is possible as all registers are memory mapped, see the reference manual.

## Slide 7: How do I... Check for memory usage?
Check linker memory report
Use debugger to check the stack
Use debugger to set memory watch
Notes:
See RTOS presentation for RTOS specific memory usage.
See Speaker Notes for details.
Discussion:
Again, how can a memory watch be used here?
Notes: Notes
See https://mcuoneclipse.com/2013/04/14/text-data-and-bss-code-and-data-size-explained/ for the explanation of the linker memory report. Does it fit in the Flash / SRAM of your board?
Use ‘info frame’ to get info on the stack and ‘p $sp’ to the current stackpointer.
Use ‘info files’ to get the different memory segments. See the device datasheet for the memory map of your device.
Setting a memory watch can be very useful when a global variable seems to be overwritten due to a memory problem like stack overflow. This often will result in HardFault_Handler() being called.

## Slide 8: How do I... Check other stuff like hardware setup, register settings?
Use research methods, see http://ictresearchmethods.nl
Discussion:
What kind of research methods can be useful?
Notes: Notes
To find the right hardware setup and register settings many research methods can be used, see http://ictresearchmethods.nl. Some examples:
  Literature study, start with the data sheets available.
  Prototyping, create small proof of concepts.
  Data analytics, measure in- and outputs with measuring equipment to verify hardware and software interact as expected.
  Hardware validation, check if the hardware is working as expected, for instance with a ‘Hello World!’ like program.
  Expert interview, ask an expert when the standard approach does not seem to work.
  Root cause analysis, use the flow diagrams in this presentation or maybe a fishbone diagram.

## Slide 9: Common bugs
See Speaker Notes for the (non trivial) common bugs!
Notes: Board bricked some pins are already occupied. On the NUCLEO-F303RE board for example pin PA2, PA3, PA13 and PA14 are already programmed to connect to USART2_TX and USART2_RX and ST-LINK respectively. When accidently overwriting the PA2 / PA3 / PA13 / PA14 settings this can leave the board ‘bricked’. In this case pushing the reset button on the board while powering up might help. This will force the board entering the bootloader again after which a new program can be uploaded. Using STM32CubeIDE one can see which pins are already in use in the default configuration, see the GPIO presentation.
Pins not working Pins configured / used before hardware is initialized with SystemClock_Config(), MX_GPIO_Init() and MX_USART2_UART_Init(). Watch out when creating class objects outside the main. The constructor is then called before the main is executed in which you might do hardare configurations. You can still create a class object outside the main, but then use a .Setup() or .Begin() fuction (also often done with Arduino libraries) which can be called after the hardware is properly initialized.
Hardware setup wrong If your button / LED / servo does not seem to work, please check first the setup with the use of measuring equipment. An LED you can connect simply to the power supply to check if it is ok. DO NOT FORGET THE RESISTOR!
Side effects Please check if you do not introduce side effects when setting bits in a register, use appropriate bit masking techniques!
Code gets stuck Code can get stuck in a loop or interrupt handler. Please use prints or the debugger to check this.

## Slide 10: Summary
Do not use the ‘trial and error’.
Take the time to check this presentation and follow the steps.
Only ask for help when you have a concrete question and can show what you already did to narrow down the problem!

## Slide 11: And finally
Notes:   The bad news: Debugging can be very time consuming and lead to a lot of frustration and you probably cannot avoid it completely. You will have to get through .
  The good news: The time you spent on defensive programming, version control and (unit) testing will definitely be earned back!