GPIO challenge

2023-09-25
Karlo Koelewijn
Content

- Title page	pg 1
- Content	pg 2
- Introduction	pg 3
- Research	pg 3-7
- Design	pg 8
- Tests	pg
- Reflection	pg
- Sources	pg

Introduction

This challenge is meant to become familiar with the Nucleo-F303RE. By learning to use CMSIS (low level register manipulation) to set pins and control its functions. The STM32 micro-controller has a single Arm Cortex M4 core and provides direct access to the registers.

research
requirements
- showing output
  - possible ways
    - serial output
    - led
- receiving user input
  - possible ways
    - polling (not allowed due to assignment)
    - interrupts
- allowed HAL functions
  - HAL_UART_Transmit()
    - used to print text to the serial monitor.
  - HAL_getTick()
    - used to get the time since power on in micro-seconds.

## Showing output

We have 2 ways we need to display output, using the serial monitor and setting a pin as output and setting the output high. We got an example how to write to the serial in the project template we received.
Fig 1. Source
The other way we have to display output is through a led turning on and off. We can achieve that using CMSIS on the Nucleo by manipulating the registers. Specifically the GPIOx (where x is replaced by a letter from A to H) to select which gpio block we want to use. In the GPIOx we have the MODER (mode register) and the OTYPER (Output Type Register).
The MODER is a 32bit register with 2 bits per pin, the 2 bits are used to determine the function of the pin. There are 4 options shown in Fig 2.
Fig 2. Source: nucleo f303re refrence sheet 11.4.1 on pg 237

After setting the MODER we have to set the OTYPER (16bit register) with one of the following values:
Fig 3. Source: nucleo f303re refrence sheet 11.4.2 on page 238

By setting the MODER to input mode and the OTYPER to push-pull we are able to digitally read the pin like an Arduino with digital-read, using the IDR (Input Data Register) by bit-masking it we can set the pin on or off.

## Taking user input

To enable digital input we need 2 known registers and a new one.
We know the GPIOx and MODER and how to set them. We only have to use the correct values for the chosen pin and MODER setting. After that we can continue with the PUPDR (Pull Up Pull Down Register) to set a pull up or a pull down register. We can use a pull up to have 3.3v on the pin and connecting it through the button to ground. This is possible because the pull-up resistor is between 40 and 50KΩ.
The PUPDR is a 32bit register with 2 bits per pin and can be set with the following values:
Fig. 4 Source: nucleo f303re refrence sheet 11.4.4 on page 238/239

Polling for input would be the easiest to program, be seeing as it is not allowed by the assignment we need to interrupts. To configure an interrupt we have set a pin to input and set some values in the following registers: SYSCFG (system configuration controller), EXTICR (External Interrupt Configuration Register), EXTI (Extended interrupts and events controller). Inside EXTI we have the following registers: RTSR (Rising Trigger Selection Register), FTSR (Falling Trigger Selection Register), IMR (Interrupt Mask Register).
Using the SYSCFG we can access the 4 EXTICR registers and each register is responsible for 4 pins as each is a 32bit register with the top 16 bit reserved.
Fig. 5 Source: nucleo f303re reference sheet page 249.
pin 0-3 are in EXTICR1, pin 4-7 are in EXTICR2, pin 8-11 are in EXTICR3, and pin 12-15 are in EXTICR4.
RTSR/FTSR are 32 bit registers for setting the Rising/Falling edge trigger for the interrupt.
NOTE: bits 23 up to and including 28 are reserved and should not change.
Fig. 6 Source: nucleo f303re reference sheet page 298.
The IMR is a 32 bit register for masking off interrupts, 23 up to and including 28 are set to 1 to enable interrupts by default.
Fig. 7 Source: nucleo f303re reference sheet page 298.

finally to finish setting up an interrupt we need to specify what line we want to enable for interrupts to trigger, this can be achieved by calling NVIC_EnableIRQ(x) where x is the line u want to enable. The end result should look something like this:
Fig. 8 Source git.fhict.nl/I517298/t-db3-2324nj-karlo-koelewijn/
all that is left to do is set the functionality of your interrupt.
Fig. 9 Source
I use my button class which has a void HandleIrq() which is marked as volatile, and all I do inside that function is set a bool to true. Then later in my main function I handle the interaction and set the bool to false.
During my research and testing my POC` I learned multiple interesting things.
- PA14 is reserved for uploading
- PA2-3 are hardware uart pins
- incorrect setup can lead to inconsistent behavior
- flipping the wrong bits provides unwanted behavior
Design

at first I designed a polling version to get myself familiar with how input and output worked on the Nucleo. Which gave me the following flowchart and class diagram:
Fig. 10 Source
Fig. 11 Source

now the interrupt version:
part 1:
part 2

Tests

For testing I used 2 different Nucleos, I have my own at home and on at school I borrowed from ISSD (student item loaning desk). All my code ran on both Nucleos and displayed the requested/required output.

Video link(link 1)
the only difference between home and at school is that I don’t have have hardware debounce capacitors at home, but my logic debounce takes care of most of it.
Reflection
…

Sources
- Fig. 1 ->
- Fig. 2 ->
- Fig. 3 ->
- Fig. 4 ->
- Fig. 5 ->
- Fig. 6 ->
- Fig. 7 ->
- Fig. 8 ->
- Fig. 9 ->
- Fig. 10 ->
- Fig. 11 ->
- Fig. 12 ->
- Fig. 13 ->
- Fig. 14 ->
- Fig. 15 ->
- Fig. 16 ->